## Slide 1
QUANTUM ERROR CORRECTION
Q-DecodeQEC
Comparative syndrome decoding + passive vs active memory correction
Real IBM Quantum repetition-code data
M0 MWPM · M1 MLP · M2 MOR router
Kaustubh Ladda | Trinexis × IEEE | IBM Qiskit Fall Fest 2026
Evidence snapshot: 26 October 2026
Q-DECODEQEC · IBM Qiskit Fall Fest 2026
01

## Slide 2
01 · PROBLEM SETUP
A small code, a practical decoding problem
Goal: infer whether the logical observable flipped from syndrome-derived detector bits.
Q-DECODEQEC · IBM Qiskit Fall Fest 2026
02
Distance-3 repetition memory
Three data qubits · two parity checks · three syndrome rounds
D0
D1
D2
Check 0 Z0Z1
Check 1 Z1Z2
Repeated measurements expose temporal changes.
Scope: bit-flip (X) errors, not arbitrary quantum noise.
One shot → one logical-flip prediction
8 detector bits
binary input
Decoder
classical CPU
0 / 1
predicted flip
CLASSICAL TRACK
ibm_marrakesh source data
4,000 train · 1,000 internal test 2,000 unlabelled final-test shots
HARDWARE TRACK
ibm_fez memory experiment
16 circuit variants · 4,000 shots Passive offline decode vs active feedback

## Slide 3
02 · METHODS
Three decoders, two controls
All methods are evaluated on the same 1,000 labelled internal-test shots.
Q-DECODEQEC · IBM Qiskit Fall Fest 2026
03
CONTROLS
No-flip baseline
Exact pattern lookup
Required decoder comparison ↓
M0
MWPM / PyMatching
Graph-based minimum-weight matching
8 detector nodes · 18 edges 8/8 hand-built syndrome tests passed
Fastest required decoder
M1
Neural MLP
Classical multilayer perceptron
(64, 64) hidden units · 4,801 parameters Decision threshold tuned on validation
Lowest internal-test point estimate
M2
MOR difficulty-aware router
Select identity, matching or neural path
Routes by detector-weight class Platt scaling calibrates probabilities
Saves some neural calls; higher latency
The final 2,000-shot holdout has no labels; it is for frozen predictions, not scoring.

## Slide 4
03 · MAIN RESULT
Decoding cuts the measured error rate sharply
Internal test: 1,000 labelled shots · logical error rate (LER) = fraction of wrong predictions.
Q-DECODEQEC · IBM Qiskit Fall Fest 2026
04
Error bars show 95% bootstrap intervals.
24.5% → 1.8%
No-flip baseline → M1 MLP
18 errors out of 1,000 shots for M1.
What the benchmark says
All three required decoders achieve LER below 3%.
M1 has the lowest point estimate: 1.8%.
Its lead over lookup is not statistically resolved.

## Slide 5
04 · INTERPRETING THE RESULTS
The best point estimate is not automatically the winner
The predeclared rule compares paired bootstrap intervals first, then uses latency to break ties.
Q-DECODEQEC · IBM Qiskit Fall Fest 2026
05
Median classical latency (batch size 1)
Measurements are Python CPU-side timings, not QPU feedback-loop latency.
Why the report selects M0
M1 vs lookup: ΔLER = −0.002 95% paired interval: [−0.005, 0.000]
INCONCLUSIVE COMPARISON
Among statistically tied required decoders, M0 is fastest at 30.3 µs p50.
Calibration improved for M2
Expected calibration error (ECE)
0.032 → 0.016
Platt scaling improved probability reliability, but did not make M2 faster: 304.3 µs p50.

## Slide 6
05 · REAL HARDWARE
Passive logging vs active correction on ibm_fez
A separate device experiment tests whether applying a conditional X inside the circuit helps the memory outcome.
Q-DECODEQEC · IBM Qiskit Fall Fest 2026
06
BACKEND
ibm_fez
PHYSICAL LINE
22–23–24–25–26
CIRCUIT SET
8 configs × 2 versions
QPU TIME
5.0 s total
PASSIVE
Measure and store syndrome history
Memory circuit
Syndrome registers
Offline decoder
M0 / M1 / M2 applied after the hardware run.
ACTIVE
Use the last syndrome to trigger conditional X
Memory circuit
Last syndrome
Conditional X gate
16 circuits × 250 shots = 4,000 shots total (2,000 per condition).
Important distinction: labelled training data came from ibm_marrakesh; this passive/active circuit experiment ran separately on ibm_fez.

## Slide 7
06 · HARDWARE FINDINGS
Active feedback helps, but offline decoding helps more
Pooled results: 2,000 shots per condition · error bars are Wilson 95% intervals.
Q-DECODEQEC · IBM Qiskit Fall Fest 2026
07
*Active-before-feedback is reconstructed from the active circuit registers; it is not a second submitted passive circuit.
25.3% → 4.8%
Active on-device correction
Large reduction versus leaving the memory uncorrected.
What matters
Passive + M0: 1.8% LER (36/2,000 errors).
Active after correction: 4.8% (96/2,000).
A last-syndrome rule can add errors on fault types that do not affect the observable.

## Slide 8
07 · REPRODUCIBILITY
Evidence and integrity were part of the experiment
The result package was designed to be auditable, not only to report a winning number.
Q-DECODEQEC · IBM Qiskit Fall Fest 2026
08
22
data files hash-verified
34
evidence files indexed
8 / 8
matching graph tests passed
2 / 2
IBM jobs re-queried and verified
Reproducibility flow
01
Audit input schema
exact detector-layout checks
02
Train / tune
fixed seeds · train-only tuning
03
Freeze + hash
models and prediction manifests
04
Verify outputs
shot alignment · job ledger
Final holdout: 2,000 rows were predicted only after model freeze. Because labels were not supplied, no final-test accuracy or LER is claimed.

## Slide 9
08 · CONCLUSION
Promising decoding gains, with honest limits
The study demonstrates a reproducible small-code workflow—not quantum advantage or scalable fault tolerance.
Q-DECODEQEC · IBM Qiskit Fall Fest 2026
09
Three findings to remember
01
Decoding works
Internal-test LER drops from 24.5% to 1.8–2.8%.
02
M1 is not a proven winner
Its 1.8% point estimate is not resolved from lookup or M0 by paired intervals.
03
Hardware correction is nuanced
Active feedback reaches 4.8%; offline M0 reaches 1.8% on passive shots.
Next steps
Collect more labelled shots across jobs and backends.
Test larger code distances and more syndrome rounds.
Refine active correction to avoid unnecessary X gates.
Profile M2 and test faster routing policies.
Thank you
Q-DecodeQEC · Kaustubh Ladda